## Slide 1: A Low-Cost Real-Time Haptic Rendering System with Physics-Based Simulation and Force Feedback
Low-cost physical haptic device
Real-time simulation and visualisation
Bidirectional force-feedback loop

## Slide 2: Why Haptic Feedback for Robotic Training?
Manipulator training often relies heavily on vision
Contact and force are difficult to communicate visually
Simulation allows safe and low-risk training
Commercial haptic devices are expensive
Visual feedback only | Visual + haptic feedback
See motion/contact | Feel resistance/contact
Limited force awareness | Physical contact cue
Safer than real robot testing | More realistic training

## Slide 3: The Challenge
Real-time bidirectional interaction.
Motion must be sensed and transmitted.
Contact force must be computed and returned.
Delay, actuator limits, and safety affect fidelity.
User
Device Sensors
MCU
Host Simulation
Haptic Engine
Torque Command
Motors

## Slide 4: Aim and Evaluation Questions
Aim:
Design, prototype, and evaluate a low-cost haptic interface for simulated robotic manipulation.
Evaluation questions:
Can the system operate around 1 kHz?
Does the force model produce predictable bounded contact?
What limits achievable haptic fidelity?

## Slide 5: System Architecture

## Slide 6: Physical Haptic Device and Embedded Control
2-DOF planar serial mechanism.
BLDC gimbal motors.
3:1 GT2 Pulley reducer
Magnetic encoder position sensing.
STM32 embedded control.
Torque clamp, slew-rate limiter, watchdog.

## Slide 7: From Virtual Contact to Motor Torque
Virtual Wall
Virtual Proxy
  Constrained to Surface
Device End effector

## Slide 8: Host Software

## Slide 9: Demonstration

## Slide 10: Key Results
Area | Result | Interpretation
Update rate | ~1KHz | Real-time loop achieved
Host Latency | 0.299 ms mean | Host computation not bottleneck
RTT | 15.60–15.67 ms | Communication dominates
Force model | 489.57 N/m, R² = 0.9973 | Matches 500 N/m target
Safety | 31 N clamp, 55 N m/s slew limit | Bounded interaction

## Slide 11: Main Bottleneck: Communication Latency
Host computation was fast; transport delay dominated the haptic loop.

## Slide 12: Haptic Rendering Validation
Motors disabled to isolate command-side force model.
Configured stiffness: 500 N/m.
Fitted stiffness: 489.57 N/m.
R² = 0.9973.
Single-depth contact remained stable: coefficient of variation = 0.026.

## Slide 13: Safety Validation
Host force command saturated at 31 N.
Firmware torque cap limited applied command.
Slew-rate limiter bounded sudden torque changes.
Watchdog set torque to zero during communication loss.

## Slide 14: Hardware Validation
Motor-enabled contact produced clear resisting feedback.
Contact penetration remained bounded under normal interaction.
Surface-following motion showed constraint behaviour.
Response was not rigid due to latency, slew-rate limiting, and belt compliance.
Belt slip occurred under higher user force.

## Slide 15: Design Trade-Offs and Limitations
15–16 ms RTT limited stable virtual stiffness.
No current sensing limited force calibration.
Belt stage introduced compliance/slip.
Damping improved stability but softened contact.
Slew-rate limiting reduced oscillation but slowed force response.

## Slide 16: CPD and Project Management
CPD
OpenGL rendering.
C++ real-time architecture.
BLDC motor control.
Haptic rendering theory.
Latency analysis.
Project adaptation
Driver integration issues.
Pivot to SimpleFOC Mini.
Hardware delays.
Actuator failure.
Integrated testing.

## Slide 17: Conclusions
Complete low-cost haptic loop built and evaluated.
Achieved real-time sensing, rendering, torque command generation, and physical feedback.
Command-side force model matched intended stiffness.
Physical interaction was bounded and usable, but not rigid or force-calibrated.
Communication latency was the dominant limitation.
Haptic fidelity depends on the whole closed-loop system.
High-rate control alone is not enough: latency, actuation, transmission, and control design jointly determine haptic fidelity.

## Slide 18: Future Work
Lower-latency communication link.
Current sensing and force measurement.
Restore full 2-DOF actuation.
Improve transmission design.
Improve proxy/contact handling.
More realistic simulator integration.
User/task-based evaluation.

## Slide 19: Questions?